## Slide 1
A Simple WiFi PHY
Midterm Presentation
Nathan Schimpf

## Slide 2
Overview
Physical-layer implementation of Wifi components
  Main focus on the Modulation-Coding Scheme
  Comparable to RF Communications Toolbox
Target Implementation
  Quadrature Amplitude Modulation: up to 256-QAM
  Orthogonal Frequency-Division Multiplexing: 52 subcarrier (20 MHz)
  Guard-time Implementation
  Hierarchical Design
  Degradation, Estimation and Recovery

## Slide 3
Technical Background
Quadrature-Amplitude Modulation (QAM)
Orthogonal Frequency-Division Multiplexing (OFDM)

## Slide 4: 802.11 Standards
Standard | Release Date | Band (GHz) | Bandwidth (MHz) | Channel Arch. | Modulation | Max. Data Rate
802.11 | 1997 | 2.4 | 20 | DSSS/FHSS | 20 | 2 Mbps
802.11b | 1999 | 2.4 | 20 | DSSS | CCK | 11 Mbps
802.11a | 1999 | 5 | 20 | OFDM | BPSK, QPSK, 16-QAM, 64-QAM | 54 Mbps
802.11g | 2003 | 2.4 | 20 | DSSS/ OFDM | BPSK, QPSK, 16-QAM, 64-QAM | 54 Mbps
802.11n | 2009 | 2.4,5 | 20,40 | OFDM | BPSK, QPSK, 16-QAM, 64-QAM | 600 Mbps
802.11ac | 2013 | 5 | 20,40,80,160, 80+80 | OFDM | BPSK, QPSK, 16-QAM, 64-QAM, 256-QAM | 6.93 Gbps

## Slide 5: Project Status
Week of | Initial Goal | Modified Goal | Met?
February 3rd | Develop QAM (tx) | Begin QAM (tx) | Yes
February 17th | Develop 52-subcarrier OFDM (tx) | Finalize QAM (tx) | Yes
February 24th | Refactor tx components | Begin OFDM (tx) | Yes
March 3rd | Midterm Presentation | Midterm Presentation | Yes
March 9th | Develop QAM (rx) | Finalize OFDM (tx) | 
March 16th | Develop OFDM (rx) | Develop OFDM (rx) | Develop OFDM (tx)
March 23rd | Guard Time | Develop QAM (rx) | Finalize OFDM (tx)
April 6th | Recovery Techniques (Frame Detection, Frequency & Phase Offset Correction) | Guard Time, Development Catch-Up | Develop OFDM (rx)
April 13th | Final Presentation | Final Presentation | Final Presentaiton
April 20th | Final Report | Final Report | Final Report

## Slide 6: Project Overview
VI Hierarchy

## Slide 7: Project Overview
Top VI

## Slide 8: Project Overview
Symbol to DataLen
Determines number of bits for OFDM symbol

## Slide 9: Project Overview
QAM Single Carrier

## Slide 10: Project Overview
QAM Single Carrier
QAM Symbol to Waveform
Over-sample QAM values
Generate pulse waveform

## Slide 11: Project Overview
QAM Single Carrier
QAM Symbol to Waveform
QAM Bit Grouping
BToUint
Build binary array of each QAM weight
Convert to unsigned Int and scale

## Slide 12: Project Overview
QAM Single Carrier
QAM Symbol to Waveform
QAM Bit Grouping
BToUint
Random Bitstream

## Slide 13: Project Overview
OFDM Tx
Top-Level OFDM
Insert Pilots
Insert Center
IFFT
Waveform Scaling

## Slide 14: Project Overview
OFDM Tx Pilot Insertion
Insert Pilots (0) at -21,-7,7,21
Insert for each symbol
Insert based on samples per symbol
Sample Halving

## Slide 15: Project Overview
OFDM Tx Pilot Insertion Center Insertion and IFFT
Insert Center (0), width 12 at 0
Insert per Symbol
Match to Samples/Symbol
Perform IFFT per Symbol

## Slide 16: Project Overview
OFDM Rx
FFT
Decimate Waveform
Outputs support Constellation and further Processing

## Slide 17: Project Overview
OFDM Rx
Downsample FFT
Reduce Samples / QAM Symbol to 2 and 1
2SPS: Debugging

## Slide 18: Project Overview
QAM Demod
Overall Conversion to Binary Stream (BitStream)

## Slide 19: Project Overview
QAM Demod
QAM Components
Removes Center Frequency
Separates Pilot and Data Subcarriers

## Slide 20: Project Overview
QAM Demod
QAM Components
Double to Integer

## Slide 21: Project Overview
QAM Demod
QAM Components
Double to Integer
QAM Symbol to Bitstream

## Slide 22: Project Overview
QAM Demod
QAM Components
Double to Integer
QAM Symbol to Bitstream
Signed to Unsigned

## Slide 23: Project Overview
QAM Demod
QAM Components
Double to Integer
QAM Symbol to Bitstream
Signed to Unsigned
Unsigned to Binary

## Slide 24: Project Overview
Array Comparison

## Slide 25
Demo Common Structures
Array & Iterative What Worked? What Didn’t Work?
  OFDM TX: inserting Pilot and Center carriers after waveform generation
  And this
Recap
Notes: Insertion after waveform: likely the cause of a lot of sampling issues on the receive side. Also ate up a lot of time calculating the insertion points

## Slide 26
Thank You